## Slide 1
AutoAnalog-RL
Automated Sizing of High-Speed Interface Circuits via Reinforcement Learning
PCIe Gen 2 (5 Gbps) receiver equalizer: one-stage CTLE + one-tap DFE · SAC agent driving ngspice · IHP sg13g2 130 nm open PDK
github.com/Foolish-Genius/al_nebula
Team: TBD
Nebula — AI/ML for Analog Circuit Design · Round 0 · 15 September 2026
Notes: 0:00–0:25 — Introduction. Show: project title / README / repository homepage.
Hello everyone. This is our project, AutoAnalog-RL — Automated Sizing of High-Speed Interface Circuits via Reinforcement Learning.
Our objective is to automatically size a PCIe Gen 2 receiver equalizer consisting of a one-stage CTLE and a one-tap DFE, using reinforcement learning and circuit simulation.
Instead of manually sweeping circuit parameters, our SAC agent interacts directly with ngspice and searches for a design that satisfies the required specifications.

## Slide 2
Repository and overall flow
0:25 – 1:00
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 2
al_nebula/
rl/ specs, reward, environment, DFE, PVT, LLM
spice/ ngspice adapter and every measurement gate
netlists/ CTLE topology (SPICE template)
scripts/ train_sac, evaluate_policy, baselines, demo
tests/ 59-test regression suite (no ngspice needed)
tools/ OpenVAF link shim (Windows OSDI build)
docs/ report, deck, video shot list
Flow: action → device values → SPICE netlist → gates in fail-fast order → metrics → reward → agent
Simulator: IHP sg13g2 130 nm, PSP103 via OpenVAF/OSDI in ngspice 47, 8 processes, ~0.6 s per step
(brief allows IHP or sky130; PSP103 through OSDI was the fast path)
SAC agent
Environment
SpiceEvaluator
.op → .ac → PRBS .tran
→ eye/DFE → HD3
ngspice ×8
Outputs
LLM frontend: feedback → reward weights
Notes: 0:25–1:00 — Repository and overall flow. Show: GitHub repository → folders rl/, spice/, netlists/, scripts/, tests/.
This is our project repository.
The rl folder contains the specifications, reward function, environment, DFE and PVT implementation. The spice folder handles the simulator interface and measurements, while netlists contains the circuit topology.
The main training and evaluation scripts are inside scripts, and we also have a regression test suite.
The overall flow is: the SAC agent generates a normalized design action, the evaluator converts it into circuit parameters, generates the SPICE netlist, and runs the simulations. The resulting circuit metrics are then converted into a reward and sent back to the agent.
Show: architecture diagram.
The simulator uses the IHP sg13g2 130-nanometer open PDK with PSP103 models, running through ngspice.
[ADDED] The brief allows either IHP or sky130; our synopsis named sky130 — we built on IHP because its PSP103 Verilog-A models run through ngspice's OSDI interface at about 0.6 seconds per RL step.

## Slide 3
Circuit and parameters
1:00 – 1:35
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 3
Parameter | Range
W_in input width | 0.5 – 50 µm
R_load | 100 – 1000 Ω
I_bias | 0.1 – 2 mA
R_s degeneration | 10 – 500 Ω
C_s degeneration | 1 fF – 1 pF
DFE tap (6th, equalizer) | −0.5 … +0.5
1 .op
DC operating point
fail fast
2 .ac
peaking @ Nyquist,
power
3 PRBS7 .tran
lossy channel → eye,
one-tap DFE
4 HD3
100 MHz tone,
once others pass
Gates run in this order; a design that fails early costs no further simulation.
Notes: 1:00–1:35 — Circuit and parameters. Show: CTLE circuit diagram.
The circuit being sized is a differential NMOS CTLE with resistive loads and RC source degeneration.
The agent controls five CTLE parameters: input transistor width, load resistance, bias current, source degeneration resistance, and source degeneration capacitance.
For the complete equalizer, a sixth parameter is added for the one-tap DFE.
At every step, the evaluator checks the design progressively: first the DC operating point, then AC response and peaking, followed by the PRBS transient through the lossy channel, eye measurement and DFE, and finally the HD3 linearity check.

## Slide 4
RL training: the SAC loop, live
1:35 – 2:25
python scripts/demo_rollout.py reports/sac-ihp-pvt — run live: random design, random PVT corner
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 4
AutoAnalog-RL policy rollout model=sac_final.zip specs: eye >= 0.25 V, width >= 0.7 UI, peaking 3-12 dB, power <= 2 mW, HD3 <= -30 dB
start: random design (seed 21), corner SS_1.00V_62.5C
step W_in R_load I_bias R_s C_s peak dB power mW eye V eye UI HD3 dB reward specs
----------------------------------------------------------------------------------------------------
1 27.62u 829 0.46m 307 885f 5.25 0.55 0.173 0.66 - -1.64 OK:peak OK:peak<12 OK:power --:width --:eye --:hd3
2 24.05u 912 0.65m 263 786f 5.17 0.78 0.246 0.76 - -1.41 OK:peak OK:peak<12 OK:power OK:width --:eye --:hd3
3 23.24u 977 0.84m 232 688f 4.97 1.01 0.321 0.80 -57.8 20.21 OK:peak OK:peak<12 OK:power OK:width OK:eye OK:hd3
all specs met after 3 simulation step(s) in 7.0 s of wall time
sized netlist header:
* AutoAnalog-RL sized CTLE
3 sims
to meet every spec
7 s
wall time on a laptop
SS / 1.0 V / 62 °C
random corner, random start
Reward = −Σ wᵢ·violationᵢ − power charge + success bonus + margin bonus
DC failure: −10, fail fast
Notes: 1:35–2:25 — RL training demo. Show: [ADDED] run demo_rollout.py live here, then the training screenshots and learning curves on the next slide.
Now we move to the main part of the project — the reinforcement learning loop.
We use a Soft Actor-Critic, or SAC, agent. The agent starts from a random circuit design and learns which parameter changes improve the circuit performance.
The reward considers the specification violations as well as power and the margin from the required specifications.
We also use fail-fast simulation, so a design that already fails an early gate does not unnecessarily spend simulation time on the later analyses.
[ADDED, while the demo runs] Each line is one ngspice evaluation of a new design; the checklist on the right shows which specs pass. From a random start at a random corner, every spec is met within a few simulations and the sized netlist is written.

## Slide 5
Training converges in ~2k steps; 60/60 rollouts feasible over three seeds
1:35 – 2:25
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 5
~2k steps
to converge, every run
60 / 60
rollouts feasible, 3 seeds
2.53 ± 0.06
steps to feasibility (mean over seeds)
95 %
of training steps meet every spec
Notes: Show: learning curve / reward curve / feasible fraction (and a live-training capture from reports/screenshots if you want to show it ran).
The training converges in approximately two thousand environment steps. Across the three base seeds, all 60 out of 60 deterministic rollouts reached a feasible design, with an average of about 2.5 steps to reach feasibility.
These plots show the reward and feasibility improving during training, demonstrating that the agent is learning rather than simply performing a blind sweep.

## Slide 6
Result: post-channel eye diagram
2:25 – 3:15
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 6
0.327 V
eye height (target ≥ 0.25 V)
0.88 UI
eye width (target ≥ 0.7 UI)
Two-UI eye after the −10 dB channel, PRBS7 at 5 Gbps, seed-1 policy design. Measured against the transmitted bits: opening = min(ones) − max(zeros) at the best sampling phase.
Notes: 2:25–3:15 — Show actual circuit results. Show: eye diagram first.
Here is one of the key outputs — the post-channel eye diagram.
For the seed-1 design, the measured eye height is about 0.327 volts with an eye width of 0.88 UI, which satisfies our internal target of 0.25 volts and 0.7 UI.

## Slide 7
Result: AC response and peaking
2:25 – 3:15
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 7
4.2 dB
peaking at 2.5 GHz (target 3–12 dB)
5.23 dB
at 1.25 GHz after retuning (--spec nyquist_frequency_hz=1.25e9)
Peaking = gain at Nyquist − DC gain, CTLE alone (channel bypassed for the AC gate). Tunable 1.25–2.5 GHz: the 2.5 GHz design gives only 2.87 dB at 1.25 GHz; the retuned policy moves R_s 182 → 365 Ω.
Notes: Show: AC response plot.
Next is the AC response. The design shows approximately 4.2 dB of high-frequency peaking at the 2.5 GHz Nyquist frequency, which is within our required 3 to 12 dB range.
[ADDED] The Nyquist frequency is a specification input: retargeting the same policy to 1.25 gigahertz, PCIe Gen 1, gives 5.23 dB of peaking where the 2.5 gigahertz design gave only 2.87, with 20 out of 20 rollouts feasible.

## Slide 8
Result: 45 PVT corners and the design summary
2:25 – 3:15
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 8
Run | Rollouts | Steps | Best design
seed 1 / 2 / 3 | 60/60 | 2 – 3 | 0.32–0.35 V · 1.2–1.3 mW · 45/45
HD3 enforced | 20/20 | 2.5 | 0.335 V · 1.24 mW · −58 dB · 45/45
PVT curriculum | 24/24 @ corners | 2 | 0.370 V · 1.12 mW · −61.9 dB · 45/45
Equalizer (+DFE) | 20/20 | 3 | 0.355 V post-DFE · 1.36 mW · 45/45
Retune 1.25 GHz | 20/20 | 2 | 5.23 dB · 0.350 V · 1.28 mW · 45/45
5 process × 3 supply (±5 %) × 3 temperature (0 / 62.5 / 125 °C) = 45 corners; every corner inside the 3–12 dB window. Curriculum: stage 1 nominal, stage 2 a random corner per episode.
45 / 45
corners pass
24 / 24
rollouts @ random corners
Notes: Show: 45-corner plot / validation table, then the results table.
The design is then validated across the complete 45 PVT corners. The peaking remains within the required range across all of these corners.
[ADDED] The policy was also fine-tuned across all 45 corners: in evaluation, 24 of 24 rollouts that started at random corners reached a feasible design in a median of 2 steps.
For the curriculum-trained design, the best result has an eye height of 0.370 volts, power of 1.12 milliwatts, and HD3 of minus 61.9 dB, while passing all 45 PVT corners.

## Slide 9
DFE: the complete equalizer
3:15 – 3:45
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 9
Transmitter
PRBS7, NRZ
5 Gbps
Channel
2-section RC
−10 dB @ Nyquist
CTLE
5 sized values
peaking 3–12 dB
Sampler
UI-centre samples
aligned to the bits
1-tap DFE
y[n] − tap · d[n−1]
tap sized by the agent
Eye vs. bits
min(ones) − max(zeros)
bit errors counted
0.327 → 0.455 V
eye with a swept tap of +0.075, zero bit errors
0.51 V
post-DFE eye held during equalizer training (CTLE-only ≈ 0.35 V)
Two measurement flaws found by the agent and fixed:
• HD3: 2.5-cycle rectangular FFT window → leakage floor at −25 dB on every design. Integer-cycle Hann window → −58 dB (28 dB margin).
• DFE eye: labelled by the DFE's own decisions → a large tap 'opens' the eye by itself. Agent pushed the tap to +0.5 with 54/127 bit errors. Now measured against the transmitted bits; zero eye on any error.
Notes: 3:15–3:45 — DFE demo. Show: CTLE → channel → DFE diagram and DFE eye plot.
We also extended the system to size the complete equalizer by adding a one-tap DFE.
Importantly, we corrected the eye measurement so that the DFE eye is evaluated against the transmitted PRBS bits rather than the DFE's own decisions.
With the corrected measurement, the DFE still provides a real improvement. One example improves the eye height from 0.327 volts to 0.455 volts with a tap of approximately plus 0.075, with no bit errors.
[ADDED] We found and fixed two measurement flaws this way, by letting the agent exploit them: an FFT leakage floor that had faked an HD3 failure at minus 25 dB — the real value is minus 58 — and the self-labelled DFE eye, where the agent pushed the tap to its bound while the receiver got 54 of 127 bits wrong.

## Slide 10
Compared with conventional search
3:45 – 4:20
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 10
Method (random starting designs) | First feasible design | Per new instance
SAC policy (144 rollouts) | median 2–3, worst 5 | 2–3 simulations, no search
CMA-ES, random start (6 trials) | median 9, worst 24 | ~10 to feasible; 400 to refine
Random search (3000 designs) | #27 (7.9 % feasible) | ~13 per feasible design
AC-only bounded search (pre-ML) | never reaches the eye | 0.160 V post-channel eye
• 3–4× fewer simulations than CMA-ES from the same starts; ~10× fewer than random
• CMA-ES matches the policy's training-best quality given 400 sims per design — the policy's advantage is amortisation: train once, then 2–3 sims per new instance
• AC-only optimisation cannot see the eye: 0.160 V vs 0.327 V for the policy
AC-only search: 0.160 V / 0.58 UI
Notes: 3:45–4:20 — Compare with conventional search. Show: SAC vs random / CMA-ES graph and table.
Finally, we compare the RL policy against conventional search methods.
Random search requires about 13 simulations per feasible design, while CMA-ES requires around 9 simulations from random starting points.
In comparison, the trained SAC policy reaches a feasible design in a median of 2 to 3 simulations, without performing a new optimization search for every starting point.
We also tested the pre-ML AC-only bounded search. Although it could optimize the AC response, its resulting post-channel eye was only 0.160 volts, showing why optimizing only frequency-domain characteristics is not sufficient.

## Slide 11
Reproducibility and the final output
4:20 – 4:45
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 11
python scripts/train_sac.py --model-source ihp --eye-height-min 0.25 --hd3 --timesteps 12000 --n-envs 8 ...
python scripts/train_sac.py ... --corners all --resume reports/sac-ihp-hd3/sac_final.zip --timesteps 8000
python scripts/evaluate_policy.py reports/sac-ihp-pvt --rollouts 24 --baseline reports/baseline-ihp-3000
python scripts/reward_from_feedback.py "power matters much more than eye margin" --output reports/reward.json
* AutoAnalog-RL sized CTLE
* model source: ihp_ngspice
* W_in = 2.01908e-05
* R_load = 1000
* I_bias = 0.000930072
* R_s = 260.642
* C_s = 3.2956e-13
.param VDD=1.2
X1 outP inP sourceP 0 sg13_lv_nmos W=2.01908e-05 L=0.13u
X2 outN inN sourceN 0 sg13_lv_nmos W=2.01908e-05 L=0.13u
RdegP sourceP tail 260.642
...
sized_ctle.sp — the deliverable schematic
• validation.json — every gate result, 45-corner PVT, HD3, noise, area
• steps.csv / monitor files / checkpoints — the whole training trajectory
• budget_curve, eye, AC, PVT plots — PNG + CSV
• evaluation.json — rollouts, steps to feasibility, per-corner breakdown
• reward.json — weights from plain-language feedback (LLM frontend)
• 59 tests run without ngspice: python -m pytest -q
Notes: 4:20–4:45 — Reproducibility / final output. Show: terminal command → generated sized_ctle.sp → JSON/CSV/PNG output.
The entire flow is reproducible through the scripts in our repository.
The training and evaluation scripts generate JSON, CSV and PNG evidence, and every validated design also produces a sized SPICE netlist containing the circuit parameters, model information and DFE tap.
So the final output is not just an RL score — it is an actual sized circuit together with its simulation and validation results.
[ADDED, optional 15 s] Show the LLM frontend: run reward_from_feedback.py with a sentence such as "power matters much more than eye margin" and show the weights JSON that feeds --reward-settings.

## Slide 12
Summary
4:45 – 5:00
AutoAnalog-RL · Nebula: AI/ML for Analog Circuit Design · Round 0 · 12
2 – 3 sims
from a random start to every spec met
45 / 45
PVT corners, every design
sized_ctle.sp
an actual circuit, not a score
• SAC agent + ngspice gates in fail-fast order, on the real IHP sg13g2 PSP103 models
• Eye 0.32–0.37 V after a −10 dB channel, 3–12 dB peaking, ~1 mW, HD3 ≈ −60 dB, noise 0.24 mV rms
• Curriculum across 45 corners · tunable Nyquist 1.25–2.5 GHz · one-tap DFE in the action · LLM reward frontend
• Random search ~13 and CMA-ES ~9 simulations per feasible design; the policy 2–3, with no per-instance search
• github.com/Foolish-Genius/al_nebula — report, deck, 59 tests, every artifact
Thank you
Notes: 4:45–5:00 — Closing. Show: final result summary / repository.
To summarize, AutoAnalog-RL combines reinforcement learning, SPICE simulation and PVT-aware validation to automatically size a high-speed receiver equalizer.
Our trained policy achieves feasible designs in only a few simulations, passes the required circuit specifications and all 45 PVT corners, and produces a corresponding sized netlist.
Thank you.